Alternating bit protocol – corrupt messages
- Contents of each segment
  - Data segments
  - Control segments
Type, Seq. number
CRC
Type, Seq. number
CRC
© O. Bonaventure, 2008
CNP3/2008.3.

---
Alternating bit protocol : Sender
Wait
for
OK0
Wait
for
D(0,...)
Data.req(SDU)
send(D(1,SDU))
start_timer()
Wait
for
OK1
Wait
for
D(1,...)
recvd(C(OK0))
or timer expires
send(D(1,SDU))
restart-timer()
Recvd(C(OK0))
cancel_timer()
Data.req(SDU)
send(D(0,SDU))
start_timer()
Recvd(C(OK1))
cancel_timer()
Recvd(C(OK1))
or timer expires
send(D(0,SDU))
restart_timer()

---
Alternating bit protocol : Sender + CRC
Wait
for
OK0/NAK
Wait
for
D(0,...)
Data.req(SDU)
send(D(1,SDU,CRC))
start_timer()
Wait
for
OK1/NAK
Wait
for
D(1,...)
Recvd (C(NAK)) or
recvd(C(OK0))
or timer expires
send(D(1,SDU))
restart-timer()
Recvd(C(OK0))
cancel_timer()
Data.req(SDU)
send(D(0,SDU,CRC))
start_timer()
Recvd(C(OK1))
cancel_timer()
Recvd(C(NAK)) OR
Recvd(C(OK1))
or timer expires
send(D(0,SDU,CRC))
restart_timer()
All corrupted
segments are discarded in all states

---
Alternating bit protocol : Receiver
Recvd(D(1,SDU))
Send(C(OK1))
Recvd(D(0,SDU))
Send(C(OK0))
Recvd(D(0,SDU))
Data.ind(SDU)
Process
SDU0
OK
Wait
for
D(0,...)
Wait
for
D(1,...)
Process
SDU1
OK
-
Send(C(OK0))
Recvd(D(1,SDU))
Data.ind(SDU)
-
Send(C(OK1))

---
Alternating bit protocol : Receiver + CRC
Recvd(D(1,SDU,CRC))
AND IsOK(CRC,SDU)
Send(C(OK1))
Recvd(D(0,SDU,CRC))
AND IsOK(CRC,SDU)
Send(C(OK0))
Recvd(D(0,SDU,CRC))
AND IsOK(CRC,SDU)
Data.ind(SDU)
Process
SDU0
OK
Wait
for
D(0,...)
Wait
for
D(1,...)
Recvd(D(?,SDU,CRC))
AND
Not(IsOK(D(SDU,CRC)))
-
Process
SDU0
KO
Process
SDU1
KO
Process
SDU1
OK
Recvd(D(?,SDU,CRC))
AND
Not(IsOK(D(SDU,CRC)))
-
-
Send(C(OK0))
Recvd(D(1,SDU,CRC))
AND IsOK(CRC,SDU)
Data.ind(SDU)
-
Send(C(OK1))
-
Send(C(NAK))
-
Send(C(NAK))

---
 A bit of Practice
1. Amazon provides the `S3 storage service where
2. companies and researchers can store lots of
3. information and perform computations on the stored
4. information. Amazon allows users to send files
5. through the Internet, but also by sending hard-disks.
7. Assume that a 1 Terabyte hard-disk can be delivered
8. within 24 hours to Amazon by courier service.
10. Assume than hard-disks are sent over a perfect network layer
11. service where the only constraints are :
  1. The maximum segment size is 1500 bytes,
  2. The network layer header is 40 bytes (IPv6) or 20 bytes (IPv4).
12. What is the minimum bandwidth required of this service to
13. match the bandwidth of the courier service over IPv6 ? Over IPv4 ?
15. What is the goodput of the service ?

---
A bit of practice
1. Several large datacenters operators have
2. announced that they install servers as
3. containers with each container hosting up to
4. 2000 servers. Assuming a container with 2000
5. servers and each storing 500 GBytes of data,
6. what is the time required to move all the data
7. stored in one container over one 10 Gbps link ?
9. What is the bandwidth of a truck that needs 10
10. hours to move one container from one
11. datacenter to another.

---
Performance of the alternating bit protocol
- What is the performance in kb/s of ABP in this case :
  - One-way delay : 250 msec
  - Physical layer throughput : 50 kb/s
  - segment size : 1000 bits
Data
250 msec
1000/50000 = 20 msec
520 msec
Ack
-> Performance is function of
        bandwidth * round-trip-time

---
How to improve the alternating bit protocol ?
- Use a pipeline
- Principle
  - The sender should be allowed to send more than one segment while waiting for an acknowledgement from the receiver
A B
Data.ind(a)
Data.req(a)
...
D(0,a)
...
D(4,e)
Data.req(b)
Data.req(e)
Data.ind(e)